## Slide 1
Ethernet & Wireless Networking
A Comprehensive Guide to Wired & Wireless Infrastructure, Standards, Protocols, and Troubleshooting

## Slide 2
Ethernet Foundations
Ethernet Standards (IEEE 802.3), speeds, and common network hardware deployments.
Cabling & Connectors
UTP, STP, Fiber Optics, RJ-45, LC, SC, ST, and T568A/B wiring standards.
Wireless Networking
Wi-Fi Standards (Wi-Fi 4 to Wi-Fi 7), SSIDs, frequency channels, and spectrums.
Security & Troubleshooting
WPA2/WPA3 protocols, signal interference sources, and step-by-step troubleshooting.
Main Topics Covered

## Slide 3
Key Concept: Ethernet remains the backbone of modern enterprise networks due to its unmatched bandwidth consistency and immunity to radio interference.
Definition: Ethernet is the dominant wired networking technology used to interconnect devices.
Network Type: Primarily used in Local Area Networks (LANs) for high-speed local communication.
Hardware Required: Uses physical cables, RJ-45 connectors, network interface cards (NICs), and switches.
Core Benefit: Provides predictable, low-latency, high-reliability connection compared to wireless.
What is Ethernet?

## Slide 4
Workstations
Connecting office desktops and engineering workstations for latency-sensitive file access.
Data Servers
Linking enterprise database and cloud servers to network switches at 10G+ speeds.
Network Printers
Providing centralized, dedicated network connectivity for shared office peripherals.
IP Surveillance
Powering and transmitting video from IP security cameras using Power over Ethernet (PoE).
Common Uses of Ethernet

## Slide 5
Standard Name | Max Speed | Cable Requirement | Primary Application
10BASE-T | 10 Mbps | Cat3 / Cat5 UTP | Legacy Ethernet networks
100BASE-TX | 100 Mbps | Cat5 / Cat5e UTP | Fast Ethernet (Legacy LANs)
1000BASE-T | 1 Gbps (1,000 Mbps) | Cat5e / Cat6 UTP | Gigabit Ethernet (Standard LAN)
10GBASE-T | 10 Gbps | Cat6a / Cat8 UTP | Enterprise Workstations & Servers
100G Ethernet | 100 Gbps+ | Fiber Optic Cable | Data Center Backbones & ISPs
Rule of Thumb: Higher transmission speeds require higher quality cable shielding and enhanced switch hardware.
Ethernet Standards (IEEE 802.3)

## Slide 6
Cable Selection Factors
UTP (Unshielded Twisted Pair): Most common copper cable; budget-friendly and easy to install.
STP (Shielded Twisted Pair): Features metallic foil wrapping to eliminate EMI noise.
Fiber Optic: Transmits light pulses via glass fibers for extreme speeds and long distances.
•
Required Speed: 1 Gbps vs 10 Gbps+
•
Distance: <100 meters (Copper) vs Kilometers (Fiber)
•
EMI Environment: Heavy machinery / power lines present?
•
Budget Constraints: UTP < STP < Fiber Optic
Ethernet Cable Types Overview

## Slide 7
Common UTP Categories
Cat5e: Up to 1 Gbps @ 100m (100 MHz)
Cat6: Up to 10 Gbps @ 55m (250 MHz)
Cat6a: Full 10 Gbps @ 100m (500 MHz)
Cat8: Up to 25/40 Gbps @ 30m (2000 MHz)
Structure: 4 color-coded pairs of copper wire twisted around each other to reduce internal crosstalk.
Key Advantages: Very low cost, lightweight, highly flexible, and universally standardized.
Best For: Home networks, office environments, and standard patch panels.
Unshielded Twisted Pair (UTP)

## Slide 8
What is STP?
STP copper cable wraps individual wire pairs (or the overall cable bundle) in conductive metallic foil or braided wire mesh.
This barrier absorbs Electromagnetic Interference (EMI) and Radio Frequency Interference (RFI) from power lines and heavy equipment.
Pros vs. Cons
Advantages: Exceptional noise resistance in industrial settings; higher integrity over longer distances.
Disadvantages: Higher cost than UTP, stiffer to bend during installation, and strictly requires proper ground termination.
Shielded Twisted Pair (STP)

## Slide 9
Light Transmission: Transmits pulses of light through ultra-pure glass or plastic strands rather than electrical currents.
Immense Bandwidth: Capable of 100 Gbps+ speeds across dozens of kilometers without signal degradation.
100% EMI Proof: Entirely immune to electrical interference, lightning strikes, and cross-talk.
Two Core Types:
• Single-mode (SMF): Narrow core, laser light, ultra long distances.
• Multimode (MMF): Wider core, LED light, cost-effective for data centers.
Fiber Optic Cable

## Slide 10
Feature | UTP (Unshielded Copper) | STP (Shielded Copper) | Fiber Optic
Medium | Twisted Copper Wire | Shielded Copper Wire | Glass / Plastic Core
Relative Cost | Low (Most Economical) | Medium | Higher (Specialized SMF)
EMI Protection | Low (Susceptible) | High (Shielded) | Complete Immunity
Max Distance | 100 Meters | 100 Meters | Up to 40+ Kilometers
Installation | Very Easy & Flexible | Moderate (Requires Ground) | Specialized / Precision
UTP vs. STP vs. Fiber Optic

## Slide 11
RJ-45
Standard 8-position, 8-contact connector used for Ethernet UTP/STP cables worldwide.
LC Connector
Lucent Connector: Small Form Factor (SFF) push-pull connector popular in high-density switches.
SC Connector
Subscriber Connector: Square snap-in connector widely used in telecom and datacom environments.
ST Connector
Straight Tip: Older round bayonet twist-and-lock fiber connector common in legacy installations.
Network Connectors

## Slide 12
Wiring Standards
Standardized by TIA/EIA for pinout consistency:
Cable Types
T568A: GW, G, OW, B, BW, O, BRW, BR
T568B: OW, O, GW, B, BW, G, BRW, BR
Straight-Through Cable: Same pinout (T568B-T568B) on both ends. Connects different devices (Host to Switch).
Crossover Cable: T568A on one end, T568B on the other. Connects similar devices (Switch to Switch).
Auto MDI-X: Modern switches automatically detect required wire pairs, eliminating the need for crossover cables!
RJ-45 Pinouts & Cable Wiring

## Slide 13
Wireless LAN (WLAN): Wi-Fi connects devices using high-frequency radio waves instead of physical cables.
Radio Frequency Bands: Operates primarily in 2.4 GHz, 5 GHz, and newly added 6 GHz spectrums.
Universal Access: Connects smartphones, laptops, IoT sensors, tablets, smart TVs, and medical equipment seamlessly.
Flexibility vs Security: Provides maximum mobility, but requires robust encryption as data travels through open air.
What is Wi-Fi?

## Slide 14
Standard | Marketing Name | Frequencies | Max Speed (Theoretical)
IEEE 802.11n | Wi-Fi 4 | 2.4 GHz / 5 GHz | 600 Mbps
IEEE 802.11ac | Wi-Fi 5 | 5 GHz | 6.9 Gbps
IEEE 802.11ax | Wi-Fi 6 / 6E | 2.4 GHz / 5 GHz / 6 GHz | 9.6 Gbps
IEEE 802.11be | Wi-Fi 7 | 2.4 GHz / 5 GHz / 6 GHz | 46 Gbps+
Note: Newer standards introduce technologies like OFDMA and 320 MHz channels to handle dense, high-device environments efficiently.
Evolution of Wi-Fi Standards

## Slide 15
WEP (Wired Equivalent Privacy): Severely flawed & deprecated. Easily cracked in minutes. Never use.
WPA / WPA2: Introduces TKIP & strong AES encryption. Standard for over a decade.
WPA3: Modern gold standard. Features SAE (Simultaneous Authentication of Equals) to prevent brute-force attacks.
Wireless Security Protocols

## Slide 16
Definition & Purpose
SSID stands for Service Set Identifier. It is the human-readable 32-character name broadcast by access points to identify a wireless network.
Security Considerations
Connecting users select the SSID and enter credentials.
Important Myth: Hiding an SSID (disabling broadcast) is not a true security measure, as network scanners easily detect hidden packet headers.
Examples: Campus_Guest, Office_5G, Home_Network
What is an SSID?

## Slide 17
2.4 GHz Band
Only 3 non-overlapping channels (1, 6, 11). Extremely prone to congestion from microwaves & Bluetooth.
5 GHz Band
Offers 20+ non-overlapping channels. Less congestion, wider bandwidth, but shorter signal propagation through walls.
6 GHz Band
Introduced in Wi-Fi 6E/7. Unlocked huge clean spectrum with up to 1,200 MHz of bandwidth for ultra-low latency.
Wi-Fi Channels & Spectrum

## Slide 18
Common Sources of EMI
Effects & Remediation
Overlapping Neighboring Wi-Fi Networks
Microwave Ovens & Bluetooth Dongles
Concrete Walls, Metal Mirrors, and Tinted Glass
Effects: High latency, packet loss, frequent drops, slow throughput.
Remediation: Switch to channels 1, 6, or 11; migrate clients to 5/6 GHz bands; reposition Access Points central to clients.
Wi-Fi Interference

## Slide 19
Physical Checks
Ensure Wi-Fi toggle is ON & AP has power / ethernet connection.
Authentication
Verify SSID name & confirm correct WPA2/WPA3 password entry.
Signal & Range
Check RSSI signal strength; move closer to reduce attenuation.
Channel Analysis
Scan for co-channel interference & switch AP to clean channel.
Driver / Firmware
Update network NIC drivers and Access Point firmware version.
Troubleshooting Wireless Issues

## Slide 20
"Connected to Wi-Fi, but internet is extremely slow."
Solution Applied: Relocated user to 5 GHz band, changed AP to non-overlapping Channel 11, and rebooted local gateway.
Step 1: Check RSSI (Received Signal Strength Indicator)
Step 2: Analyze AP channel saturation (Channel 6 is overcrowded).
Step 3: Test router uplink speed.
Real-World Troubleshooting Scenario

## Slide 21
Ethernet (Wired)
Wi-Fi (Wireless)
Maximum stability & low latency
High bandwidth (up to 100 Gbps)
Zero device mobility
Higher physical cabling cost
Ultimate device mobility & convenience
Rapid deployment for guests & mobile
Vulnerable to radio interference
Requires strict encryption policies
Wired (Ethernet) vs. Wireless (Wi-Fi)