## Slide 1: Installing Motherboards and Connectors & Installing System Devices

## Slide 2: What is a Motherboard?
Definition: A motherboard is the main circuit board that connects all components of a computer system.
Functions:
  Distributes power to components
  Hosts CPU, RAM, and expansion slots
  Provides connectors for I/O devices
Form Factors:
  ATX: Full-sized board with many expansion slots
  Micro-ATX: Smaller with fewer slots
  Mini-ITX: Compact form, used in small builds

## Slide 4: Key Components on a Motherboard
CPU Socket: Where the processor is installed (Intel LGA, AMD AM4, etc.)
RAM Slots: Usually 2-4 DIMM slots for system memory
Chipset: Controls communication between CPU, RAM, storage
Power Connectors:
24-pin ATX main power
4/8-pin CPU power
Expansion Slots:
PCIe x16 for GPUs
PCIe x1 for network, sound cards
Storage Connectors:
SATA for HDD/SSD
M.2 for NVMe SSDs

## Slide 5: Common Cable Types in PCs
Power Cables:
24-pin ATX
4/8-pin EPS (CPU power)
Molex (legacy power for fans, older drives)
Data Cables:
SATA (modern storage)
IDE/PATA (legacy)
Front Panel Connectors:
USB 2.0 / 3.0 headers
HD Audio
Power switch, reset switch, HDD LED

## Slide 6: How to Install a Motherboard
Step 1: Prepare the case
  Install I/O shield on rear panel

## Slide 7
Step 2: Align motherboard with standoffs
Step 3: Secure with screws

## Slide 8
Step 4: Connect power cables

## Slide 9
Step 5: Connect front panel headers

## Slide 10
Step 6: Install CPU, RAM, and storage

## Slide 11: Older Cable Interfaces
IDE (PATA): 40-pin ribbon cable for older HDDs/ODDs
Floppy Drive Cables: 34-pin
Serial Ports: For older peripherals like modems
Parallel Ports: Printers and scanners
Compatibility Notes:
  Use adapter cards for modern motherboards
  Limited support in modern BIOS

## Slide 12: Maintaining BIOS Settings
CMOS Battery:
  Small CR2032 battery
  Retains BIOS settings when powered off
Jumpers:
  Clear CMOS jumper to reset BIOS
  Configured by shorting 2 pins with cap

## Slide 13: BIOS vs UEFI
BIOS (Basic Input Output System):
Text-based, keyboard-only
Limited to 2.2TB drives
UEFI (Unified Extensible Firmware Interface):
Graphical interface
Supports secure boot, network booting
Handles drives over 2.2TB
Key Settings:
Boot order
CPU/RAM diagnostics
Drive modes (AHCI/RAID)

## Slide 14: Understanding and Installing Power Supplies
Types of Power Supplies:
  Modular: Cables can be added/removed as needed
  Semi-Modular: Essential cables are fixed; others modular
  Non-Modular: All cables are permanently attached
Wattage Calculation:
  Use PSU calculators (like from Cooler Master or PCPartPicker)
  Consider GPU, CPU, and future expansion

## Slide 15: Power Supply Connectors
24-pin ATX Connector: Main power for motherboard
4/8-pin CPU Connector (EPS12V): Powers CPU
PCIe Connectors (6-pin/8-pin): Power for graphics cards
SATA Power Connectors: Modern drives (HDDs, SSDs)
Molex Connectors: Legacy devices (fans, older drives)

## Slide 16: System Board Components
Bus architecture
Chipsets
Expansion slots
Memory slots and cache
Central processing units and processor sockets
Power connectors
Onboard non-volatile storage connectors (such as for hard drives)
Motherboard headers
BIOS/UEFI/firmware
CMOS and CMOS battery
Front-panel connectors and headers

## Slide 17: Bus Architecture
A bus is a communication system that transfers data between components.
Types:
Data Bus: Transfers actual data
Address Bus: Carries memory address information
Control Bus: Manages control signals
Internal Buses: Connect CPU, RAM, and chipset
External Buses: Used for expansion cards and peripherals (e.g., PCIe)

## Slide 18: Chipsets
Coordinates data flow between CPU, RAM, storage, and I/O.
Traditional Design:
Northbridge: Manages high-speed interfaces (CPU, RAM, GPU)
Southbridge: Handles slower devices (USB, SATA, audio)
Modern Chipsets:
Single chip architecture
Integrated memory and PCIe controllers in the CPU

## Slide 19: Expansion Slots
Purpose: Allow additional cards to be installed (GPU, sound, NIC, etc.)
Common Types:
PCIe x16 – Graphics cards
PCIe x1 – NICs, USB cards
Legacy PCI – Rare in modern systems
PCIe Versions: 3.0, 4.0, 5.0 — higher bandwidth each gen

## Slide 20: Memory Slots and Cache
Memory Slots:
Called DIMM (Dual In-line Memory Module) slots on desktops
SODIMM (Small Outline Dual In-line Memory Module) for laptops
Support dual/quad channel
Cache Memory:
L1/L2/L3: Located on CPU
Function: Stores frequently used instructions to reduce access time

## Slide 22
67.6 mm
260 Pins
133.35 mm
288 Pins

## Slide 24: Memory Slots and Cache Contd...
Types of Cache Memory:
Level 1 Cache:
Fastest and smallest type of cache.
Located directly on the processor die.
Integrated into the CPU core itself—closest possible location for maximum speed.
Stores both instructions and data.
Typical size: 80 KB total (e.g., 32 KB for instructions, 48 KB for data per core).
Dedicated to each core — not shared

## Slide 25: Memory Slots and Cache Contd...
Types of Cache Memory:
Level 2 Cache:
Larger but slower than L1 cache.
Still located on the CPU die in modern processors.
Typical size: 512 KB per core.
Usually dedicated per core, but in some architectures, it's shared between cores.
Acts as an intermediate layer between L1 and L3.

## Slide 26: Memory Slots and Cache Contd...
Types of Cache Memory:
Level 3 Cache:
Largest and slowest among the cache hierarchy.
Size: typically 8–16 MB.
Shared among all cores of a processor.
Allows efficient communication and data exchange between CPU cores.

## Slide 27: Memory Slots and Cache Contd...
Type | Location | Size Range | Speed | Shared/Dedicated
L1 Cache | On processor die | ~80 KB | Fastest | Dedicated per core
L2 Cache | On processor die | ~512 KB | Very fast | Usually per core
L3 Cache | On processor die | 8–16 MB | Slower | Shared across all cores

## Slide 29: Central Processing Units (CPUs)
Executes system instructions
Installed into CPU socket on motherboard
Key specs: Clock speed, cores/threads, cache, TDP
Comes in Intel or AMD varieties

## Slide 30: Processor Socket
LGA (Land Grid Array) – Intel CPUs
PGA (Pin Grid Array) – AMD CPUs
BGA (Ball Grid Array) – Non-removable, soldered
Socket must match CPU model
Motherboard BIOS may need updating for newer CPUs

## Slide 31: Power Connectors
Distribute power from PSU to motherboard and components
Main 24-pin ATX power connector
4/8-pin CPU power connector
SATA power connectors for drives
PCIe power connectors for graphics cards

## Slide 32: Onboard Non-Volatile Storage Connectors
Connectors for storage drives that retain data after power-off
SATA III – Standard for SSDs and HDDs
M.2 – For NVMe SSDs (faster, smaller)
U.2, mSATA – Older/enterprise connections
Connected directly to chipset or CPU (for NVMe)

## Slide 33: Motherboard Headers
Internal connectors used for:
USB headers (USB 2.0, 3.0, 3.2)
Audio headers (front panel audio)
Fan headers (CPU_FAN, SYS_FAN)
RGB/LED headers
Header types differ in pin count/layout

## Slide 34: BIOS, UEFI
BIOS (Basic Input/Output System): Legacy firmware
UEFI (Unified Extensible Firmware Interface): Modern, GUI-based
Functions:
Hardware initialization
Boot sequence
Configuration utility
Stored in non-volatile flash memory

## Slide 35: CMOS & CMOS Battery
CMOS (Complementary Metal-Oxide Semiconductor):
Stores BIOS/UEFI settings (time, date, boot order)
Battery (CR2032):
Powers CMOS chip when system is off
If dead, BIOS resets to defaults

## Slide 36: Front-Panel Connectors and Headers
Connect case to motherboard:
Power switch
Reset switch
HDD activity LED
Power LED
Connected via small pin headers (e.g., F_PANEL)
Must follow manual for correct pin layout

## Slide 37: Cooling Components and Installation
Types of Cooling Systems:
Air Cooling: Heatsinks with fans (common and budget-friendly)
Liquid Cooling: Closed-loop or custom (efficient, expensive)
Passive Cooling: No fans (low-power builds only)
Installing Cooling:
Apply thermal paste (pea or line method)
Mount CPU cooler onto socket
Attach and align case fans (intake/exhaust)

## Slide 41: Connecting Storage Components
Drive Types:
HDD: High capacity, slower
SSD (SATA): Faster, common upgrade
NVMe (M.2): Fastest, uses PCIe lanes
Mounting Drives:
Use brackets, screws or trays
Secure properly in drive bays or M.2 slot
Cable Connections:
SATA Data + SATA Power
M.2/NVMe needs only screw and PCIe lane slot

## Slide 42: Setting Up Storage in BIOS/OS
BIOS/UEFI Detection:
Confirm storage is detected in BIOS
Windows/Linux Setup:
Use Disk Management (Windows)
Use lsblk, fdisk, mkfs (Linux)
RAID (Redundant Array of Independent Disks):
RAID 0 (striping), RAID 1 (mirroring), RAID 5 (parity)
Requires multiple drives and RAID-capable board/controller

## Slide 43: Understanding RAM Installation
RAM Types:
  DDR3 (older), DDR4 (current mainstream), DDR5 (newer, faster)
RAM Channels:
  Single, Dual, Quad channel setups for better performance
Installation Tips:
  Match RAM speed and size
  Insert in correct slots (check motherboard manual)
BIOS Check:
  Ensure full capacity detected
  Enable XMP Profile for correct speed

## Slide 44: CPU Installation Guide
Intel vs AMD Sockets:
  Intel (LGA1700, LGA1200), AMD (AM4, AM5)
Installation Steps:
  Lift socket arm/cover
  Align notches and gently insert CPU
  Lock down with arm or retention mechanism
  Apply thermal paste and install cooler

## Slide 45: Managing System Thermals
Thermal Paste Application:
  Pea-sized dot or line in the center
  Avoid over-application
Airflow Planning:
  Front: Intake, Rear/Top: Exhaust
  Maintain positive/neutral pressure
Fan Placement Tips:
  Use dust filters, align airflow
  Connect fans to headers (CPU_FAN, SYS_FAN)

## Slide 46: Final System Build Checklist
Cable Management:
Route cables behind motherboard tray
Use zip ties or Velcro straps
Screw Types:
Motherboard screws, M.2 screws, case screws
Post-Build Checks:
POST screen appears
Fans spinning, LEDs on
BIOS recognizes all components