## Slide 1
UNIT 01 · SERVER INFRASTRUCTURE
Server Hardware & Infrastructure
Components, form factors, and installation & configuration — with real hardware from Dell, HPE, Meta, Cisco, and NVIDIA
01U
Dell PowerEdge R660 · Intel Xeon Scalable
02U
HPE ProLiant DL380 Gen11 · Dual Redundant PSU
04U
Dell PowerEdge XE9680 · 8× NVIDIA H100
SERVER.HW — FIELD GUIDE

## Slide 2
Agenda
01
Server Hardware
Components, characteristics, why hardware matters, and where it's used
02
Server Form Factors
Tower, rack mount, and blade — features, applications, and comparison
03
Installation & Configuration
CPU, RAM, bus types, bus channels, expansion slots, and applications
SERVER.HW

## Slide 3
01 · FOUNDATIONS
Understanding Server Hardware
A server is a computer system that provides resources, services, or applications to other computers (clients) over a network. Server hardware is engineered to support demanding workloads and uninterrupted operation — built from interconnected components that process data, store information, and manage network communication.
Unlike consumer hardware, these components are designed with redundancy, expandability, and fault tolerance — because servers often run 24 hours a day, 7 days a week, making reliability and efficient resource management critical design requirements.
TECH EXAMPLE
A Dell PowerEdge R760 ships with dual hot-swap 800W PSUs and an integrated iDRAC9 controller — an admin elsewhere can reboot it, reflash firmware, or watch fan speeds without walking to the rack.
SERVER.HW — 01 FOUNDATIONS

## Slide 4
01 · FOUNDATIONS
Key Characteristics of Server Hardware
1
High Reliability
Continuous operation, minimal downtime
2
Scalability
Add CPUs, memory, storage as needs grow
3
Redundancy
Duplicate PSUs and drives prevent outages
4
Performance
High-core CPUs, fast storage, ample RAM
5
Remote Management
Monitor and configure without physical access
6
Serviceability
Hot-swap parts cut maintenance time
SERVER.HW — 01 FOUNDATIONS

## Slide 5
01 · FOUNDATIONS
Major hardware components
Component | Purpose | Tech example
CPU | Executes instructions & processes workloads | Intel Xeon Platinum 8592+ (64 cores)
RAM | Temporarily stores active data & applications | Samsung 64GB DDR5 ECC RDIMM
Storage | Permanently stores OS, apps, and data | Samsung PM1743 NVMe U.2 SSD (Gen5)
NIC | Connects the server to the network | Broadcom NetXtreme-E 100GbE adapter
Motherboard | Connects and links all components | Supermicro X13DEi dual-socket board
PSU | Provides stable electrical power | Delta 1100W Titanium, redundant pair
Cooling System | Removes excess heat, maintains safe temps | Microsoft two-phase immersion cooling
Expansion Slots | Allow extra network/storage controllers | PCIe Gen5 x16 hosting NVIDIA H100
RAID Controller | Manages drives for performance & protection | Dell PERC H965i / Broadcom MegaRAID
SERVER.HW — 01 FOUNDATIONS

## Slide 6
01 · FOUNDATIONS
Why it matters to a server administrator
Server administrators ensure hardware resources meet organizational requirements. Proper server hardware lets them:
✓
Maintain continuous availability of critical services with minimal downtime
✓
Support multiple users and applications simultaneously by efficiently managing resources
✓
Improve overall system performance with sufficient processing power, memory, and storage
✓
Minimize hardware failures through redundancy and backup components
✓
Simplify maintenance and future upgrades with minimal disruption
✓
Support virtualization and enterprise workloads running multiple VMs and demanding applications
SERVER.HW — 01 FOUNDATIONS

## Slide 7
01 · FOUNDATIONS
Applications in server environments
File Servers
Centralized file storage and sharing, letting authorized users securely access files from different locations.
Web Servers
Host websites and web applications, delivering content and online services over a network.
Database Servers
Manage large volumes of structured data for efficient storage, retrieval, and processing.
Application Servers
Run enterprise software and provide the resources required to support business applications.
Virtualization Platforms
Host multiple virtual machines on one physical server, improving hardware utilization.
Cloud Infrastructure
Provide scalable computing and storage services allocated on demand.
SERVER.HW — 01 FOUNDATIONS

## Slide 8
02 · PHYSICAL DESIGN
Server Form Factors
A server form factor is the physical design, size, and mounting style of a server — determining how it's installed, organized, cooled, and managed. Choosing the right one affects space, scalability, maintenance, and power efficiency.
01
Tower
Standalone, desktop-like footprint
02
Rack Mount
Measured in Rack Units, stacks in a cabinet
03
Blade
Shares power & cooling in a chassis
SERVER.HW — 02 FORM FACTORS

## Slide 9
02 · PHYSICAL DESIGN
Tower Server
Resembles a traditional desktop computer but is built with enterprise-grade hardware, standing vertically as an independent server.
FEATURES
Standalone — no shared chassis or rack needed
Simple installation, no specialized equipment
Easily accessible for upgrades and repairs
Supports moderate hardware expansion
Suited to limited, small-scale workloads
APPLICATIONS
Small businesses needing reliable operations
Branch offices for local network services
Educational institutions
Small departmental file/print servers
Testing and development environments
TECH EXAMPLE
Dell PowerEdge T350 or HPE ProLiant ML350 Gen11 are common picks for a branch office running a single file-and-print server.
SERVER.HW — 02 FORM FACTORS

## Slide 10
02 · PHYSICAL DESIGN
Rack Mount Server
Installed inside a standardized server rack. Measured in Rack Units (U), where 1U = 1.75in (44.45mm). Common sizes: 1U, 2U, 4U.
FEATURES
High space efficiency — many servers, one rack
Standardized rack installation
Centralized cable management
Easier maintenance in data centers
Good scalability by adding units
APPLICATIONS
Enterprise data centers
Web hosting companies
Database servers
Application servers
Virtualization platforms
Cloud computing environments
TECH EXAMPLE
Dell PowerEdge R760 (2U) and HPE ProLiant DL360 Gen11 (1U) are the default building blocks of most enterprise data centers.
SERVER.HW — 02 FORM FACTORS

## Slide 11
02 · PHYSICAL DESIGN
Blade Server
A compact server module that slides into a shared blade chassis, sharing power, cooling, networking, and management hardware.
FEATURES
Extremely compact per-server footprint
Shared power and cooling infrastructure
Very high server density
Simplified, centralized management
Efficient shared cable management
APPLICATIONS
Large enterprise data centers
Cloud service providers
High-performance computing (HPC)
Large virtualization environments
Private cloud infrastructure
TECH EXAMPLE
Cisco UCS B-Series and Dell PowerEdge MX7000 pack a dozen-plus compute nodes per chassis for large virtualization farms.
SERVER.HW — 02 FORM FACTORS

## Slide 12
02 · PHYSICAL DESIGN
Form factors compared
Feature | Tower | Rack Mount | Blade
Installation | Standalone | Mounted in server rack | Installed in blade chassis
Space utilization | Low | High | Very high
Scalability | Moderate | High | Very high
Initial cost | Low | Moderate | High
Cable management | Basic | Organized | Minimal — shared infra
Shared power/cooling | No | No | Yes
Best suited for | Small organizations | Medium-large enterprises | Large data centers & cloud
SERVER.HW — 02 FORM FACTORS

## Slide 13
02 · PHYSICAL DESIGN
How form factor choice evolves
GROWTH SCENARIO
A company initially operates a single file server using a tower server. As the business grows, additional services such as database and web hosting are introduced, requiring multiple servers. The organization upgrades to rack mount servers for better space utilization and centralized management. A large cloud service provider, however, uses blade servers to maximize computing density while reducing power consumption and cable complexity.
TECH EXAMPLE
Meta's Open Compute Project (OCP) pushes the blade concept further, standardizing rack-scale designs that Meta, Microsoft, and Rackspace all deploy to cut both cost and cabling complexity.
SERVER.HW — 02 FORM FACTORS

## Slide 14
03 · DEPLOYMENT
Installation & Configuration
Server performance and reliability depend not only on high-quality hardware but also on correct installation and configuration. Proper installation ensures the server operates efficiently, while correct configuration allows the OS to recognize and use installed hardware effectively. Improper installation can cause hardware failures, reduced performance, or system instability.
CPU
RAM
Bus Types
Bus Channels
Expansion Slots
SERVER.HW — 03 DEPLOYMENT

## Slide 15
03 · DEPLOYMENT
CPU
LGA4677 · SP5
The CPU is the primary processing component of a server — it executes OS instructions, processes application workloads, and manages communication between hardware. Enterprise servers may support one or more processors depending on motherboard design.
INSTALL
1
Power off & disconnect all power
2
Open the server chassis safely
3
Locate the CPU socket
4
Align processor to the socket notch
5
Seat CPU without applying force
6
Lock the socket retention mechanism
7
Apply thermal paste if needed
8
Install heat sink & cooling fan
9
Reconnect the fan cable
CONFIGURE
✓
Verify BIOS/UEFI detects the processor
✓
Confirm model and clock speed
✓
Enable supported CPU features
✓
Ensure OS recognizes all cores/threads
TECH EXAMPLE
4th-Gen Intel Xeon Scalable "Sapphire Rapids" uses socket LGA4677; AMD EPYC 9004 "Genoa" instead uses socket SP5 — not interchangeable.
SERVER.HW — 03 DEPLOYMENT

## Slide 16
03 · DEPLOYMENT
RAM
DDR5 ECC RDIMM
RAM temporarily stores data and instructions actively used by the processor. Servers commonly use ECC (Error-Correcting Code) memory, which detects and corrects errors to improve reliability.
INSTALL
1
Power off the server
2
Open chassis to access memory slots
3
Identify correct slots per documentation
4
Align notch with the slot
5
Press evenly until clips lock
6
Follow recommended slot population order
CONFIGURE
✓
Verify total installed memory in BIOS/UEFI
✓
Ensure modules run at supported speeds
✓
Confirm OS detects installed RAM
✓
Check ECC memory is functioning correctly
TECH EXAMPLE
Samsung and SK hynix 64GB DDR5 ECC RDIMMs are standard picks in Dell and HPE servers, correcting single-bit memory errors on the fly.
TECH EXAMPLE
ECC memory in Dell and HPE servers logs correctable errors to iDRAC/iLO, letting admins spot a failing DIMM before it causes an outage.
SERVER.HW — 03 DEPLOYMENT

## Slide 17
03 · DEPLOYMENT
Bus Types
A bus is a communication pathway that transfers data, addresses, and control signals between hardware components within the server.
Bus Type | Function
Data Bus | Transfers actual data between the CPU, memory, and peripheral devices, enabling information to move efficiently during processing.
Address Bus | Carries memory addresses from the CPU to identify the location of data, ensuring information is accessed correctly.
Control Bus | Transmits control signals that coordinate hardware operations, such as read and write commands.
CONFIGURATION
✓
Ensure hardware compatibility with the motherboard
✓
Verify BIOS/UEFI correctly detects installed devices
✓
Install appropriate chipset drivers if required
TECH EXAMPLE
PCIe Gen5 lanes act as a high-speed data bus connecting CPUs to NVMe drives and GPUs at up to 32 GT/s per lane.
SERVER.HW — 03 DEPLOYMENT

## Slide 18
03 · DEPLOYMENT
Bus Channels
Bus channels are communication paths that allow simultaneous data transfer between hardware components. More channels mean more bandwidth.
Single Channel
One communication channel — basic bandwidth for standard workloads
Dual Channel
Two channels simultaneously — faster data transfer
Triple Channel
Three channels — higher bandwidth for demanding tasks
Quad Channel
Four channels — significant bandwidth for enterprise workloads
Multi-Channel Architecture
Uses multiple channels at once to maximize memory bandwidth
CONFIGURATION
✓
Install identical memory modules for compatibility
✓
Insert into manufacturer-recommended paired slots
✓
Verify BIOS/UEFI reports the correct channel mode
✓
Confirm OS recognizes the configured memory
TECH EXAMPLE
Intel Xeon Scalable CPUs run 8-channel DDR5; AMD EPYC "Genoa" runs 12-channel DDR5 — more channels raise bandwidth at the same clock speed.
SERVER.HW — 03 DEPLOYMENT

## Slide 19
03 · DEPLOYMENT
Expansion Slots
Connectors on the motherboard that allow additional hardware devices to be installed, increasing the server's functionality.
TYPICAL DEVICES
Network Interface Cards (NICs)
RAID Controllers
Graphics adapters
Fibre Channel adapters
Storage controllers
INSTALL
1
Power off the server
2
Remove the expansion slot cover
3
Align the card with the slot
4
Insert firmly until fully seated
5
Secure with retaining screw
6
Close chassis, reconnect power
CONFIGURE
✓
Verify BIOS/UEFI detects the device
✓
Install required device drivers
✓
Confirm OS recognizes & loads the device
✓
Perform basic functional testing
TECH EXAMPLE
An NVIDIA H100 GPU seats in a PCIe Gen5 x16 slot in a Dell PowerEdge XE9680; a Broadcom ConnectX-7 400GbE NIC occupies a smaller x8 slot alongside it.
SERVER.HW — 03 DEPLOYMENT

## Slide 20
03 · DEPLOYMENT
Applications in server environments
Database Servers
Require multiple processors and large amounts of RAM for high-speed transaction processing.
Virtualization Hosts
Use multi-core CPUs and high-capacity memory to run multiple virtual machines efficiently.
Web Servers
Use expansion cards such as high-speed network adapters to support large volumes of client requests.
Enterprise File Servers
Benefit from properly configured memory channels to improve data access performance.
SERVER.HW — 03 DEPLOYMENT

## Slide 21
REFERENCE
Glossary for students
A few extra terms worth knowing when working with real server hardware.
BIOS/UEFI
Firmware that initializes hardware at boot and hands control to the OS.
ECC
Error-Correcting Code — memory that detects and fixes single-bit errors.
RAID
Redundant Array of Independent Disks; e.g. RAID 1 mirroring, RAID 5 parity, RAID 10.
iDRAC / iLO
Dell's/HPE's out-of-band controllers for remote monitoring and control.
PCIe Lane
A serial data path in PCI Express; more lanes (x8, x16) mean more bandwidth.
Hot-swap
Replacing a component while the server keeps running, with no downtime.
NVMe
A storage protocol for flash memory over PCIe, far faster than SATA/SAS SSDs.
Rack Unit (U)
Standard measurement of rack-mount equipment height; 1U = 1.75 inches.
SERVER.HW — REFERENCE

## Slide 22
SUMMARY
Hardware, form, and setup — together they define a server's reliability.
Redundant, serviceable components (Dell PERC RAID, dual Delta PSUs) keep services running through failure.
Form factor — tower, rack, or blade — is chosen by scale: a Cisco UCS blade chassis serves very different needs than a Dell PowerEdge T350 tower.
Correct CPU sockets, ECC memory, and matched channel configurations (Intel 8-channel, AMD 12-channel DDR5) let the hardware perform at spec.
Every install step ends in a configuration check — BIOS/UEFI detection, driver installation, and OS recognition confirm the hardware is actually usable.
SERVER.HW — FIELD GUIDE